## Slide 1: ECE 477 Final Review: Team #15
Caleb Shinkle Software Lead
Seth Deegan Team Lead
Nathan Huang Hardware Lead
Brian Lu Systems Lead

## Slide 2: Outline
Project Overview
Block Diagram
Design Challenges
Individual Contributions
Project Video Demonstration
Questions

## Slide 3: Project Overview
Our project is a miniaturized version of the Altair 8800, the first commercially successful personal computer from MITS in 1974. It is an actual microcomputer that can be programmed from its front switches.
Artist Rendition
Final Product

## Slide 4: Project Overview (Hardware)
Our project differs from the original Altair 8800 by:
Emulating the functionality of the original hardware
  RP2350B microcontrollers housed on custom PCBs
  All software written in Rust
Using modern bus voltages
  All logic on 3.3V as opposed to +/- 16V, +/- 8V, etc.
Reducing the form factor
  More condensed/portable

## Slide 5: Project Overview (Software)
We ended up using 3 major software packages for our final design:
Interchange: Front Panel Software
  Polls all buttons/switches on front panel, forwards appropriate information to the bus
​Cycle: Intel 8080 CPU Emulator
  Listens to bus signals, communicates with memory, and emulates all instructions in the 8080's instruction set
Recall: RAM Software
  Listens for and responds to memory requests on the bus
​
Each of these packages runs on its own microcontroller, and they communicate over a 44-signal bus facilitated by a backplane PCB
The packages control GPIO pins to communicate with each other

## Slide 6: Block Diagram (Cards to Backplane)

## Slide 7: Block Diagram (FUll Backplane Interface)
Card PCBs (CPU, RAM, etc.)
Front Panel

## Slide 8: Block Diagram (Front Panel to Backplane)

## Slide 9: Design Challenges
Hardware
  KiCad 8.0.0 → 9.0.0 → 8.0.0 (backport)
  Dense routing requirements for front panel
  Flipped QSPI Connections
  Improper Solder Paste
  Sink Driver Chips
  Incorrect Button Pins
Software
  Programmable I/O
  Debugging Frameworks
  Immature Rust tooling
  CPU ⇔ RAM Bus Communication

## Slide 10: Individual contributions
Bus read/write transaction logic and code
Front panel logic and code
Learned and applied Rust RP2350 programming framework, Embassy
Learned and applied probe-rs, OpenOCD debugging tools
Created team bus transaction chart, Gannt chart, documentation
Seth Deegan
Notes: <TO-DO>

## Slide 11: Individual contributions
Initial project proposal and general system design
Wire harnessing of initial breadboard prototype
Design of microcontroller section and final layout/route of card and front panel PCBs
Mechanical integration of PCBs into pre-defined enclosure
PCB assembly and bodges
Microcontroller bringup
Some software tooling
Assistance on software debugging and memory transaction routines
Brian Lu
Notes: <TO-DO>

## Slide 12: Individual contributions
Hardware Prototyping
PCB Design
PCB Manufacturing
PCB Assembly & Soldering
Mechanical Design
Nathan Huang

## Slide 13: Individual contributions
Hardware Prototyping
  Front Panel + Redesign
  Backplane
  Card
Nathan Huang

## Slide 14: Individual contributions
PCB Design
PCB Manufacturing
Nathan Huang
Front Panel
Back Plane

## Slide 15: Individual contributions
PCB Assembly & Soldering
  3 Cards (x4)
  1 Backplane (x4)
  1 Front Panel (x4)
Nathan Huang

## Slide 16: Individual contributions
Mechanical Design
  Bezel CAD
  Milling + Tapping Enclosures
  Spray Painting
Nathan Huang

## Slide 17: Individual contributions
Wrote the RAM software package, excluding bus transactions
Prototyped CPU emulator package using keyboard inputs instead of actual front panel to test instruction execution
  Nearly identical to final implementation excluding main loop
Wrote the first iteration of the front panel software's main loop to run on final hardware
  Integrated with simplified CPU emulator so we had something to demo
Worked on debugging main loops for front panel and CPU emulator communication
Caleb Shinkle

## Slide 18: Project Demonstration
PSDRs
Ability to support communication between CPU and RAM cards over a simplified S-100 inspired bus, using a backplane PCB with DDR4 DIMM edge connectors to connect bus signals between cards.
An ability to interface the RP2350B microcontroller with I2C-based MCP23017 and MCP23008 I/O expanders to reduce GPIO pin usage, allowing support of all 44 bus signals and some extras that are necessary.
An ability to provide a regulated power supply is fulfilled by the backplane board, which includes a 5V to 3.3V step-down power supply using a reference buck converter design.
An ability to emulate the Intel 8080 processor in software, written in Rust to decode and execute Intel 8080 instructions with accurate cycle timing and interrupt management. This emulator will be designed to emulate 8080 machine cycles, which respect concepts such as waiting for I/O operations.
Ability to manage parallel bus data exchange using Programmable IO (PIO) assembler routines, which are assembled and processed by the CPU, RAM, and front panel software. These routines must allow for multi-device control of the same data lines on the bus.
(Stretch):
An ability for a UART card to implement the UART protocol, using I/O control lines (separate from memory control lines), and transmit and receive the information to an external UART port.

## Slide 19: Project Demonstration VIDEO

## Slide 20
Questions?