## Slide 1: ECE477 Midterm Design Review: Team #15
Caleb Shinkle Software Lead
Seth Deegan Team Lead
Nathan Huang Hardware Lead
Brian Lu Systems Lead

## Slide 2: Outline
Project Overview
Major Components
Block Diagram
Packaging Design
Electrical Schematic
PCB Layout
Prototyping Progress
Software Development Status
Project Timeline
Questions

## Slide 3: Project Overview
αCassiopeiae: a condensed clone of the Altair 8800
Switches/LEDs on front panel for user interaction
  Instruction/Data input
  Memory examination
Smaller and lower-power
  Modern bus voltage (3.3V)
Original hardware emulated in software (Rust)
Able to run 8080 programs
  Designed for hobbyists/collectors
Alpha-Cassiopeiae

## Slide 4: PSDRs
(Hardware) Ability to support communication between CPU and RAM cards over a simplified S-100 inspired bus, using a backplane PCB with DDR4 DIMM edge connectors to connect bus signals between cards
(Hardware) Ability to interface the RP2350B microcontroller with I2C-based MCP23017 and MCP23008 I/O expanders to reduce GPIO pin usage, allowing support of all 44 bus signals and additional features.
(Hardware) Ability to provide a regulated power supply is fulfilled by the backplane board, which includes a 5V to 3.3V step-down power supply using a reference buck converter design.
(Software) Ability to emulate the Intel 8080 processor in software, written in Rust to decode and execute Intel 8080 instructions with accurate cycle timing and interrupt management. This emulator will be designed to emulate 8080 machine cycles, which respect concepts such as waiting for I/O operations.
(Software) Ability to manage parallel bus data exchange using Programmable IO (PIO) assembler routines, which are assembled and processed by the CPU, RAM, and front panel software. These routines must allow for multi-device control of the same data lines on the bus
Stretch
(Hardware) An ability for a UART card to implement the UART protocol, using I/O control lines (separate from memory control lines), and transmit/receive the information to/from an external UART port

## Slide 5: Major Components
RP2350B (QFN80 Package)
150 MHz clock frequency
512 KB SRAM
48 GPIO pins
  12 programmable I/O (PIO) state machines
2.7-5.5 V input voltage
Supports 16 MB external QSPI flash
2 UARTs
2 I2C controllers
2 SPI controllers
Microcontroller

## Slide 6: Major Components
ESP32-DOWD-V3
240 MHz clock frequency
520 KB SRAM
34 GPIO pins
  Not as many as RP2350, would require more expanders
2.3-3.6 V input voltage
3 UARTs
2 I2C interfaces
1 SPI interface
Chose RP2350 over ESP mainly due to GPIO requirements
Microcontroller Alternative

## Slide 7: Major Components
Front Panel
The front panel for our system is a PCB that will contain a RP2350, as well as the switches and LEDs necessary for user interaction
LEDs: SunLED XZM2CRK45WT-9
  Reverse-Mount LEDs (Red)
  2.2V forward voltage
  50mA forward current
Switches: Chanzon B09R3XLVVS
  Through-Hole-Mount double-throw switches
  Up to 50V, 500mA
There were lots of other switches and LEDs we could have chosen, just found ones that had the right voltage/current ratings and looked decent

## Slide 8: Major Components
Power Supply
Voltage Regulator: MCP16331
Input voltage range: 4.4-50 V
Output voltage range: 2-24 V
  Adjustable with external resistors
Up to 1.2 A output current
Up to 96% efficiency, 2% output voltage accuracy
Will use wall adapter to step down 120V AC to 5V DC
  Then use circuit with this to step from 5V DC to 3.3V DC

## Slide 9: Major Components
Power Supply alternative
Voltage Regulator: LT3045
Input voltage range: 1.8-20 V
Output voltage range: 0-15 V
Only up to 0.5 A output current
  Thought we might need more current since we have several microcontrollers, so we went with the MCP 16331

## Slide 10: Block Diagram
Bus signals controlled by PIO on all RP2350Bs
Toggle buttons include deposit, examine memory, and clock single-step switches, among others
CPU/RAM cards run CPU/RAM emulators respectively

## Slide 11: BLOCK DIagram
CARD/BACKPLANE DETAIL VIEW

## Slide 12: BLOCK DIAGRAM
PANEL/BACKPLANE DETAIL VIEW

## Slide 13: Packaging Design
Extruded ENCLOSURE

## Slide 14: ELECTRICAL SCHEMATIC
Card

## Slide 15: ELECTRICAL SCHEMATIC
Card – USB-C in

## Slide 16: ELECTRICAL SCHEMATIC
Card – POWER Regulation

## Slide 17
QSPI FLASH MEmORY

## Slide 18: Card
Full View

## Slide 19: CARD
REAR VIEW

## Slide 20: Card
USB-C

## Slide 21: Card
Regulation

## Slide 22: Card
MEmory

## Slide 23: Card
Oscilator

## Slide 24: Card
Debug, ReSet

## Slide 25: Card
Bus Layout
In Progress
Working backwards, PCB layout dictates final pin permutation

## Slide 26: Front Panel
Old Design
Taken from: https://upload.wikimedia.org/wikipedia/commons/b/b2/MITS_Altair_8800_Front_Panel.jpg

## Slide 27: Electrical Schematic
3D-View: FRONT

## Slide 28: Electrical Schematic
3D-View: BACK

## Slide 29: Electrical Schematic
3D-View: Card

## Slide 30: Front Panel
Full view

## Slide 31: Front Panel
Microcontroller (1)
Inspired by Card Schematic
Debugging and Power Regulation
Slight Modifications to Addressing

## Slide 32: Front Panel
Microcontroller (2)
New Jumper Lines
Two I2C Channels
Remapping for Status Symbols

## Slide 33: Front Panel
Sink drivers
5 TLC59211IN Sink Drivers
High output current
3-3.6 V Range
PW0020A SMD

## Slide 34: Front Panel
LED ARRAY
16 Address LEDs
8 Data LEDs
12 Status LEDs

## Slide 35: Front Panel
I/O Expansion
2 MCP23017 I/O Expanders
Offsets of 32 and 33
Connected to user inputs

## Slide 36: Front Panel
Board Connectors
Flat Flex Connectors
Staggered Power and Ground Lines
Enough Signals to carry S-100 Bus

## Slide 37: Front Panel
Reset Line
Local Net
Hard Reset on I/O Expanders and RP2350.
Active Low

## Slide 38: Front Panel
PCB LAYOUT

## Slide 39: Front Panel
SWITCHES

## Slide 40: Front Panel
SWITCHES

## Slide 41: Front Panel
Status, ADDRESS, DATA LEDS (1)

## Slide 42: Front Panel
Status, ADDRESS, DATA LEDS (2)

## Slide 43: Front Panel
Sink Drivers, microcontroller
Sink Drivers held close to Micro
Easier access to traces

## Slide 44: Front Panel
Sink Drivers, microcontroller (2)
Layout needs optimization
Complete before submission

## Slide 45: Front Panel
I/O Expanders
Same concept for Micro
I/O Lines close to inputs

## Slide 46: Front Panel
I/O Expanders (2)

## Slide 47: Back Plane
Full view

## Slide 48: Back plane
Dimm slot

## Slide 49: Back Plane
Power

## Slide 50: Back plane
Layout

## Slide 51: Back Plane
Power Layout

## Slide 52: Back Plane
3d

## Slide 53: Prototyping Progress
Switches and LEDs work as intended
  Switches and LEDs for addresses/data follow desired behavior
  Need to finish connecting to GPIO of micro running the front panel software
Any additional behavior changes we need will be implemented/debugged in software
Front Panel Prototype

## Slide 54: Prototyping Progress
2 RP2350B Stamp XL Boards
  Direct connections of bus signals just like our eventual backplane board
  Connected to breadboard to test communication between softwares (CPU emulator, RAM emulator, etc.)
2 Pico 2 Boards
  Connected to bus signals for debugging with rs-probe
Allows testing of tram (bus control package) and other software
  Doubles as test harness for our system
Backplane Prototype

## Slide 55: Prototyping Progress
Backplane Prototype
No Bus Signals Connected
Bus Signals Connected

## Slide 56: Software Architecture

## Slide 57: SoftWare learnings
It takes a lot to figure out how to emulate a full computer using newer technology!
How to program in Rust
What is async Rust
How Rust project structure works
How to program embedded devices and specifically the RP2350 with Rust
How Programmable I/O (PIO) works
8080 bus signals
8080 ISA
8080 emulator implementation
How the 8080 bus timing works
Types of bus operations we need to support

## Slide 58: Software Specifications
Runner: CPU Emulation Software
Will run on the CPU card's RP2350B
Emulates the original Intel 8080 processor
Needs to drive bus signals through tram (our bus control package) specifying machine cycles (reads/writes)
  As instructions need to access memory, machine cycles will be executed
  Gives addresses/data to tram to put on bus
Goal is to implement functionality of all Intel 8080 instructions

## Slide 59: Software Specifications
Recall: RAM Emulation Software
Will run on the memory card's RP2350B
Needs to listen to bus signals through tram specifying machine cycles (reads/writes)
  Calls local read()/write() functions to retrieve/store values from stack-allocated array
  Sends signals back to tram to put on bus

## Slide 60: Software Specifications
Interchange: Front Panel Software
Will run on the front panel's RP2350B
Needs to drive LEDs on front panel and poll I2C lines/GPIO pins to detect changes on switches
  Will also go through tram to access the bus when necessary (examining memory, etc.)

## Slide 61: Overall Software operation
CPU emulator tells tram to execute instruction
Tram takes over machine cycle operation (reading/writing memory if needed)
  Each machine cycle has different time steps, which tram will moderate
  CPU emulator waits for tram to respond
Machine cycle fetches or writes one byte
  If 3 bytes of data needed for a single instruction, it will take 3 machine cycles to complete
Sequence: Instruction Decode (runner) -> Machine Cycle (tram) -> Individual Timesteps (tram) -> Await response from memory (recall) -> return data to runner -> control given back to runner
Multiple layers of abstraction to work with

## Slide 62: Bus architecture
Bus states
Tram is responsible for moderating bus state
When Running/Always:
  CPU/MEM Read
  CPU/MEM Write
  Front/MEM Read
When in single step:
  FRONT/MEM Write
UART will have its own states, stretch goal so we will figure that out if we get to it

## Slide 63: Bus architecture
Bus Signal Table

## Slide 64: Bus architecture
READ

## Slide 65: Bus architecture
Write

## Slide 66: Machine operation
Clock always running
Single step just triggers a flip flop to have the pc attach to the main clock.
Examine sends a jmp instruction (jmp, upper, lower)
Flip On switch (deliver power to all PCBs, microcontrollers start, set front panel = stop, CPU pc = 0)
Program first instruction
  First byte
    You’re already in data mode. Flip the switches to change the data line. Lights do not change
    Hit deposit. Data lights should change to switch values.
  Second byte
    Flip switches to change data line
    Hit deposit NEXT. Address lights flip to mem address 1, data line reflects switches.
  X byte …
Examine byte
  Flip switches to address you want to examine
  Hit Examine. Data lights should change.
Running
  Hit Stop, Reset (goes to mem location 0, reset does not clear memory)
  Hit single step. Will execute machine cycle

## Slide 67: Software Development Status
In this section, detail team progress with software development. List out the major modules for your team’s software. For each module, detail its status (Not yet started / In development / In testing / Completed)
Rust packages
Tram (bus control library)
In Development
Interchange (front panel)
Not Started
Ubahn (UART Card software)
Not Started, Stretch Goal
Cycle (CPU card software)
- Not started
Runner (CPU emulator)
In Development
Recall (RAM card software)
In Development
Ready for testing once Tram is tested

## Slide 68: Project Timeline

## Slide 69: 3D Printing
Questions?